## Slide 1
Speech Signal Modeling and Processing: Fundamentals and Applications
Distinguished Lecture, 17 November 2019
Christian Ritz, School of Electrical, Computer and Telecommunications Engineering/Centre for Signal and Information Processing, University of Wollongong, Australia,

## Slide 2: Introduction to APSIPA and APSIPA DL
APSIPA Mission: To promote broad spectrum of research and education activities in signal and information processing in Asia Pacific APSIPA Conferences: ASPIPA Annual Summit and Conference APSIPA Publications: Transactions on Signal and Information Processing in partnership with Cambridge Journals since 2012; APSIPA Newsletters APSIPA Social Network: To link members together and to disseminate valuable information more effectively APSIPA Distinguished Lectures: An APSIPA educational initiative to reach out to the community

## Slide 3: First, a bit about me
Current Projects in speech and audio
Co-Prime microphone Arrays
Sound event classification
Hyperspectral image processing
Spatial audio scene analysis and coding
Wind noise modelling for microphone arrays
Machine/deep learning for cancer diagnosis from 3D medical images
Sonar image classification
Past Projects
Ad-hoc microphone arrays for speech
Classroom audio analysis for understanding student learning and interaction
Spatial Audio source separation
Multizone spatial audio
Acoustic Vector Sensors
Acoustic classification for steel industry applications (local industry collaboration)
Deputy Director, Centre for Signal and Information Processing (CSIP)
Four academic staff+PhD and postdocs with expertise in:
  Speech, audio and multimedia signal processing for enhancement, 3D and spatial audio
  Visual signal processing, pattern recognition, machine learning for radar, video, images, medical signals, human action recognition, compressive sensing, etc.
CSIP is part of our Faculty’s Signal, Information and Communications research powerhouse (SICOM)
Associate Dean, International, Faculty of Engineering and Information Sciences
Professor, School of Electrical, Computer and Telecommunications Engineering

## Slide 4: Where is Wollongong?
About 1 hour south of Sydney on the East coast of NSW
UOW: 212th in the world – QS World University Rankings 2020
World Class Engineering, 87th worldwide – THE World University Rankings by Subject for 2019
13th in the World - Times Higher Education University Impact Rankings 2019

## Slide 5: Overview
Speech technology applications
Speech production model and speech signal characteristics
Linear Prediction (LP) for modelling speech
Human sound perception
Enhancing speech corrupted by noise
Performance measures for speech processing applications
Microphones and microphone array processing of speech (bonus slides)

## Slide 6: Speech Technology Applications

## Slide 7: Speech technology applications are used in everyday life
Talking to friends on your mobile (cell) phone
Sending a short voice message using WeChat
Using Siri or other voice assistant to find information, answer a question without having to type
Automatically translating spoken Chinese to English
Automatically converting your speech to text
These applications are all based on clever digital signal processing algorithms

## Slide 8: Speech technology is big business
They are all offer and use different speech technology in their products
Notes: Finally, you might be thinking of who engineers working on digital technologies specifically for voice, images and video may work for. Here’s some you may have heard of – I’ve missed plenty!

## Slide 9: Creating speech technology applications has many challenges
In telephony, voice quality must be clear, natural and understandable
Speech recognition needs to be accurate
Compression is needed for efficient storage or transmission over wireless networks
Signal enhancement is needed so these applications work well when recording your voice in noisy environments
  E.g. background noise from cars, restaurant, wind, etc.

## Slide 10: Overcoming these challenges requires clever digital speech signal processing algorithms
Requires models of the speech production system and how this relates to characteristics of the recorded speech signal
Approaches to modeling the speech signal for compression or recognition applications
Technology for enhancing speech signals prior to further processing (speech enhancement algorithms – front-
Technology for recording speech signals (microphones)

## Slide 11: Speech production model and speech signal characteristics

## Slide 12: Modeling the speech production system or how people talk
Requires not only maths but understanding how speech is produced
Speech produced by forcing air from the lungs up through the vocal tract and out through the mouth
Different speech sounds produced by moving the speech articulators into different positions
  vocal folds, tongue, lips, teeth, jaw and other parts
Different sounds have different signal characteristics
  These should be modeled differently to ensure high quality speech applications
Don Johnson, Speech Signal Analysis. OpenStax CNX. May 18, 2013 http://cnx.org/contents/b7785f59-bfcd-4bc2-b749-141d1b2eba62@3.8.

## Slide 13: Classification of speech sounds
Two main categories: Voiced or unvoiced
Voiced sounds
  mostly include vowel sounds, e.g. the ‘o’ sound in the word ‘coding’
Unvoiced sounds
  include consonants such as the ‘p’ sound in the word ‘speech’
Speech sounds can also be categorized as different classes of phonemes
  The smallest unit of a language
  English has 40 different phonemes, categorized as vowels, dipthongs as well as different types of consonants (semivowels, nasals, stops or plosives, fricatives, africates, whispers)
Each class of phonemes has different acoustic signal characteristics
  Requires careful modeling and processing of these to ensure high quality speech signals are input to applications such as compression or recognition

## Slide 14: Speech Signals change over time – hence models must be updated regularly
Voiced speech section
Unvoiced speech section
Voiced section looks (and sounds) different to unvoiced section
So we need different models for different segments – called frames in speech coding
Approx. 350 ms of speech

## Slide 15: Analysis of speech signals
Voiced speech = periodic section
The period of the signal is the distance between the major pulse peaks and is known as the pitch period, or pitch
Unvoiced speech = random section
  no periodic structure also known as aperiodic
pitch
unvoiced
voiced

## Slide 16: Typical Speech production model
Uses a source filter model, where the source is known as the excitation
Voiced speech: periodic excitation
Unvoiced speech: aperiodic (or random) excitation
Filter is linear time varying filter that models the vocal tract
Vocal tract is like a closed tube
  as air from the lungs (excitation) passes through the tube, different sound is produced depending on how you move the vocal folds and speech articulators
Excitation source
Vocal tract tube
First 2 resonances in the tube (first 2 formants)

## Slide 17: Magnitude spectra of voiced speech
Derived from short-term Fourier transform applied to the speech signal (typically, 20 to 30 ms segment)
The envelope (dashed red curve) represents the shape of the vocal tract
The peaks in the envelope correspond to the formant frequencies, caused by the resonances occurring in the vocal tract
Accurately modeling the spectral envelope is important for ensuring high perceptual speech quality
  E.g. speech coding, speech enhancement, speech synthesis, etc.
Formant frequencies

## Slide 18: Magnitude spectra of unvoiced speech
The envelope of the unvoiced speech magnitude spectrum is generally flatter, with less clear peaks compared to voiced speech
Often, unvoiced speech can be modelled less accurately than voiced speech but still produce satisfactory speech quality
  E.g. use random white noise, with a magnitude (gain) matching the magnitude of the original unvoiced speech signal

## Slide 19: Key points from this section
Speech production model tells us how we make speech sounds
Speech sounds can be voiced or unvoiced
  Different models for each type
Voice sounds: periodic, envelope of the magnitude spectrum has distinct peaks at formant frequencies
Unvoiced sounds: aperiodic, envelope of the magnitude spectrum is flatter, with no peaks at formant frequencies

## Slide 20: Linear prediction for modeling speech

## Slide 21: Linear Prediction (LP) as used in speech coding
- input digital speech signal
- prediction of the current speech sample based on past speech samples
prediction coefficients
Key idea:
  speech signals are correlated over short durations (e.g. 20 ms)
  Storing or transmitting the residual and prediction coefficients requires less data than the input speech signal
LP Filter

## Slide 22: So LP is calculated over short durations - 20 to 30 ms length frames
Break the digital speech signal into frames
Calculate the LP coefficients, , for each frame
Calculate the residual signal
1 Frame
Other frames
The Autocorrelation method is typically used for finding

## Slide 23: The speech production model in more detail
Modelling using z-transforms:
Periodic pulse generator
Random pulse generator
Time varying digital filter
Pitch
Vocal tract parameters
s(n)
e(n)
G
voice/unvoiced switch
e(n): excitation, G: gain
s(n): speech

## Slide 24: Modelling the time-varying digital filter
The time varying digital filter is modelled using linear prediction
Taking z-transforms of the LP equations and simplifying:
LP Analysis Filter

## Slide 25: How would we do this in Matlab?
Calculate the LPC coefficients using the function lpc
  The resulting coefficients can be used in an FIR filter applied to the speech signal
Derive the residual signal using the filter function
  Input signal is the speech signal, s(n) and filter coefficients are the LPC coefficients
Practical issues to consider
  Forming speech into frames using time-windowing
  Appropriate choice of linear prediction order
  Appropriate choice of frame length

## Slide 26: Properties of Linear Prediction (LP)
LP removes the short term correlations for the input speech
Speech signal
Residual signal

## Slide 27: Properties of Linear Prediction (LP)
The magnitude spectrum of the LP filter is a representation of the envelope of the speech magnitude spectrum
Original signal
LP spectrum (dashed curve)

## Slide 28: Deriving the prediction coefficients
The LP coefficients can be derived by minimising the mean squared prediction error
  Here, N is the duration of the speech segment
Generally, N corresponds to between 160 to 200 samples for speech sampled at 8 kHz
This corresponds to 20 ms to 25 ms
In Matlab, the LP coefficients can be calculated using the function lpc
  Typically use the autocorrelation approach solved using Levinson-Durbin recursion (or some other methods)
Minimise the LP residual (error)
Solve the following:

## Slide 29: How is this used in speech coding?
Vocal tract shape and the pitch evolve much more slowly than the digital sampling rate of the speech signal
  Successive periods of the waveforms show little change and hence there is short term correlation
Hence, instead of quantising and transmitting every speech sample at a high rate, the vocal tract shape and pitch can be estimated, quantised and transmitted at a much lower rate
  Leads to coding gains (less bits needed)
Speech coder:
  Encoder: Models the speech signal (e.g. using LP), quantise and transmit the LP coefficients, pitch, residual (excitation) signal information
Today, companies implement speech coding based on international standards
Speech Encoder
Speech Decoder
speech signal
Synthesised speech signal
bitstream

## Slide 30: Key points from this section
Voice component of speech signals changes slowly over time
This can be modeled using Linear Prediction
  Uses a set of past (p) speech samples to estimate the next sample
The LP filter is a model of the vocal tract filter
  Using this model we can design efficient speech coding (compression) systems

## Slide 31: Human sound perception
How we hear sound

## Slide 32: First, how do we hear sound?
Auditory perception – how we hear sound
  Air vibrations case ear drum to vibrate
  Ear has small bones that react to these vibrations
  Fluid in cochlear moves
  Inner ear hair cells act as sensors to detect these movements
  Different ear hair cells sense different sound frequencies
Watch this video to find out the basics:
  http://www.youtube.com/watch?v=r-c5GpoD8wI&feature=share&list=PL0001168E6597D0EA

## Slide 33: Human perception of sound
Humans hear sounds in the frequency range of 50 Hz to 20 kHz
  However, not all frequencies are perceived the same
Threshold in quiet:
  The intensity of required to ensure the sound is just audible
Loudness:
  Perception of intensity (amplitude)
  Some frequencies are perceived to be louder than others
    Even though the intensity is the same
Equal loudness curves:
  Show the perceived loudness for tones (single frequency signals)

## Slide 34: Not all sounds are perceived equally
Some sounds need to have a really high amplitude before they can be heard
Other sounds can have quite a low amplitude but still be heard
So, sounds within this frequency range (main range for speech) are most perceptually important
Threshold in hearing curve –Sound Pressure Level (SPL) threshold required for a listener to first perceive (hear) are tone at each frequency (based on listening tests)

## Slide 35: Critical bands
Adjacent frequencies that are perceived similarly can be grouped into bands known as critical bands
  Lower frequencies have narrow critical bands
  Higher frequencies have wider critical bands
One critical band also known as one Bark
Equation for the Critical Band as a function of the centre frequency, , of the band:
  This tells you the bandwidth centred at
Typical conversion function [2] to convert from Hz to z Bark:

## Slide 36: Critical Bands (2)
Example of the first 6 bands and bands 18 to 21 calculated with equation on previous slide
Band No. | Centre Frequency | Critical Bandwidth | CB min. | CB max.
1 | 50 | 100 | 0 | 100
2 | 150 | 102 | 99 | 201
3 | 250 | 104 | 198 | 302
4 | 350 | 109 | 296 | 405
5 | 450 | 114 | 393 | 507
6 | 570 | 122 | 509 | 631
18 | 4000 | 685 | 3658 | 4343
19 | 4800 | 867 | 4367 | 5234
20 | 5800 | 1111 | 5245 | 6356
21 | 7000 | 1426 | 6287 | 7713
High frequencies: Wider bandwidths
Low frequencies: Narrower bandwidths

## Slide 37: Using sound perception models in speech processing
Mel-Frequency Cepstrum Coeficient (MFCC): Based on mapping the linear frequency scale to the non-uniform mel frequency scale (similar idea to the bark scale)
Key steps:
  Take the Discrete Fourier Transform (DFT) of a windowed speech frame
  Map the DFT magnitude spectrum to the mel scale
  Take the logarithm of the power at each mel frequency
  Take the Discrete Cosine Transform (DCT) of the resulting powers – the MFCCs are the magnitudes of this spectrum
The MFCC was used in many early speech recognition system and still used in applications such as sound event classification

## Slide 38: Key points from this section
Auditory perception models tell us what parts of sound are most important for a listener
Sound frequency perception is non-linear
  Can be modeled with critical bands
Models should adapt to this non-linear perception
  E.g. use cepstrum and MFCCs

## Slide 39: Enhancing speech corrupted by noise
Spectral characteristics of noise, noise and speech intelligibility, listening to noise-degraded speech, basic speech enhancement algorithms

## Slide 40: Speech in the presence of backround noise
When speech is recorded in background noise, it becomes harder to hear clearly and can affect the signal characteristics
  Makes it hard for us to clearly understand what is being spoken (reduces speech intelligibility and speech quality)
  Makes it more difficult for a computer to automatically recognize what is being spoken (reduces recognition accuracy)
We can divide noise in two categories
  Stationary - remains unchanged over time, e.g. noise from fans
  Non-stationary – the spectral characteristics of the noise change over time e.g. noise on the street changes as different vehicles pass by, different people talking at the same time, etc.
Non stationary noise: harder to deal with as the spectral characteristics change over time

## Slide 41: Spectral characteristics of noise
Chart: Frequency Hz
Different noise types have the energy concentrated in different regions – compare with spectra of male (blue curve) and female (purple curve) speech
Babble Noise: speech from many people talking around you e.g. in a restaurant
Pink Noise: Mostly low frequency
Here, the noise has amplitudes higher than the speech amplitude – this distorts the speech signal

## Slide 42: Examples of noisy speech
Let’s listen to some examples
What is the speaker saying?
Babble Noise
Factory Noise
White Noise
What affect does the noise have?

## Slide 43: Speech Enhancement Algorithms
Aim: improve the perceptual quality and intelligibility of speech that has been corrupted by noise
Classes of speech enhancement algorithms:
  Spectral Subtractive algorithms – Assume noise is additive, hence if the noise can be estimated it can be removed by simple subtraction of the noise signal from the noise corrupted signal
  Statistical based Algorithms, Subspace Algorithms and methods using source modelling
  We’ll concentrate on spectral subtractive approaches in this lecture!

## Slide 44: Spectral Subtractive Algorithms
Assume the noise corrupted signal is , which is comprised of the clean signal and additive stationary noise signal .
The noise corrupted signal can be expressed as:
Taking the discrete time Fourier transform of both sides

## Slide 45: Spectral Subtractive Algorithms
Expressing in polar form
And
The estimate of the clean speech can be expressed as:
Phase
Magnitude

## Slide 46: Spectral Subtractive Algorithms
But, both the magnitude and phase of the noise signal is unknown
  Hence we assume that the magnitude of the noise can be estimated during non-speech activity - big assumption!
  Phase of the noise is replaced by the phase of the noisy speech, .
  Assumes that phase does not affect speech intelligibility (but may affect speech quality)
Now we can express our clean signal estimate as:

## Slide 47: Spectral Subtractive Algorithms
The clean signal estimate now can be obtained from the inverse Fourier Transform of .
One problem:
  when we subtract the noise from noisy speech the result may be negative
One solution:
  use of a half wave rectifier

## Slide 48: Suppression Function Representation
We can write (13) in the following form:
Here is referred to as the gain function or suppression function
provides the amount of suppression or attenuation ( applied to the noisy power spectrum at a given frequency to obtain the enhanced power spectrum

## Slide 49: Spectral subtraction – practical limitations
Spectral subtraction is applied separately to a frame of speech
  Just like frames used in Linear Prediction
Good performance requires accurate estimation of the magnitude of the noise component
  If noise is assumed stationary, one approach is to use the average magnitude of the first 3 to 5 recorded frames (assuming no speech signal at the start)
  More sophisticated approaches regularly update the noise estimate using e.g. Voice Activity Detection (VAD) to find segments when no speech is present
Negative values owing to errors in the noise spectrum calculation creates isolated peaks in the spectrum
  when converted to time domain, this sounds like tones with frequencies that change randomly from frame to frame - known as musical noise
  Musical noise significantly degrades perceptual speech quality
Minor disadvantage:
  errors in the phase, since we use the phase of noisy speech for the output speech, produces roughness in the quality

## Slide 50: Algorithms to Reduce Musical Noise
Spectral Subtraction Using Over subtraction
  Rather than setting any negative value to 0, set to a small value (spectral noise floor)
Hence:
If energy of the frame is below the noise floor, , subtraction is not performed
  Magnitude of current frame = average magnitude of previous and future frames
One problem:
  Requires accessing future frames so can be high delay

## Slide 51: Algorithms to Reduce Musical Noise (2)
Spectral Subtraction Using Over subtraction
  Rather than setting any negative value to 0, set to a small value (spectral noise floor)
Hence :
  where is the over subtraction factor ( and is the spectral floor parameter
  The best value of was found through experimentation to be
    Where is the desired value of at 0 dB SNR

## Slide 52: Spectral Subtraction: Other methods
Non-linear spectral subtraction
  Frequency-dependent over-subtraction
Multi-band spectral subtraction
  Separate subtraction per frequency bin
Minimum mean square error spectral subtraction
  Optimal selection of and
Plus many others

## Slide 53: Key points from this section
Backround noise affects our ability to hear speech clearly or for computers to recognize speech accurately
Speech enhancement aims to reduce the affects of noise
Spectral subtraction: simplest method and based on subtracting estimated noise magnitude from recorded (noisy) speech magnitude
  Phase of the enhanced speech set equal to the phase of the recorded (noisy) speech
Various methods exist to reduce the effects of musical noise resulting from subtracting inaccurate estimates of the noise signal

## Slide 54: Performance measures for speech processing applications
Subjective and Objective methods

## Slide 55: Performance measures for speech enhancement
Speech quality
  Based (ideally) on listening tests e.g. Mean Opinion Score (MOS)
  Objective measures: the Perceptual Evaluation of Speech Quality (PESQ)
Speech intelligibility
  Both listening tests and objective measures
There are also other objective measures based on the spectrum
Speech recognition accuracy
  Typically based on the Word Error Rate (WER)

## Slide 56: Mean Opinion Score (MOS) test
The listeners are asked to grade many sentence that include original noisy speech, clean speech and output speech from the speech enhancer
  (5) Excellent
  (4) Good
  (3) Fair
  (2) Poor
  (1) Bad
The average score across all sentences is then used to grade the performance
Need many examples of coded speech sentences and many listeners
  The more the better in terms of achieving statistically significant results

## Slide 57: Perceptual Evaluation of Speech Quality (PESQ)
Objective measure, standardised by ITU
Based on perceptual models
Compares a reference speech signal with the degraded speech signal
  E.g. from the output of a speech coder
Results in an estimated listening quality MOS
  Extensive testing has shown high correlation between PESQ scores and subjective MOS when testing speech coding performance

## Slide 58: Subjective Intelligibility tests
Ask people to listen to a sentence or word and then write down what was spoken
E.g. Modified Rhyme Test (MRT) or Diagnostic Rhyme Test (DRT) using standard lists
  E.g. http://www.meyersound.com/support/papers/speech/mrtlist.htm
Objective measures of speech intelligibility also exist e.g. the short-time objective intelligibility measure (STOI)
  C. H. Taal, R. C. Hendriks, R. Heusdens and J. Jensen, "An Algorithm for Intelligibility Prediction of Time–Frequency Weighted Noisy Speech," in IEEE Transactions on Audio, Speech, and Language Processing, vol. 19, no. 7, pp. 2125-2136, Sept. 2011

## Slide 59: Other Objective Tests
The objective tests that can be used to evaluate speech quality are:
  The Signal to Noise Ratio (SNR)
  Log Spectral Distortion (LSD)
  Itakura Saito Distance (ISD)
The SNR measures a given distortion in speech
LSD and ISD are spectral envelope distortion measures

## Slide 60: Log Spectral Distortion
If is the power spectrum of the speech signal, where is the Fourier transform, then the LSD can be defined as
where is the spectral density corresponding to the processed signal
Large values of LSD resemble higher distortion and smaller values resemble smaller distortions

## Slide 61: Itakura Saito Distance
Based on the LSD, can be used as an indicator of subjective quality of speech
  It has been reported that if the ISD is less than 0.5 the difference MOS score is less than 1.6
The ISD between two signals can be expressed as:

## Slide 62: Speech Recognition Accuracy
Word Error Rate (WER): Basically, comparing output transcription (sentence) with input transcription (sentence)
  S = number of substituted words (replacing one word with another
  D = number of deleted words (complete removal of the word)
  I = number of inserted words (extra words)

## Slide 63: Key points from this section
Various methods exist for evaluating the performance of speech signal processing applications
  Includes subjective listening tests and objective signal-based measures
Important to pick the right method for the right application

## Slide 64: Microphones and microphone array processing of speech (bonus slides)
Brief introduction, Introduction to Microphone Array Signal Processing

## Slide 65: Microphones
Sensors for measuring changes that occur in the propagation of the sound waves
  Could be changes in pressure, temperature or the density
The most common type of microphones measure pressure changes
  Contain a single opening and a single diaphragm which vibrates to vary either the capacitance, resistance or magnetic field in order to generate a time varying electrical signal
This electrical signal, whose amplitude various over time, corresponds to the analog speech signal
  This is then digitally sampled to form the digital speech signal used in speech processing applications
Polar response – important property of microphones
  Response (output) of the microphone as a result of sounds arriving from different directions

## Slide 66: Omnidirectional microphones
Captures the sound signals equally from all directions
Polar response measurements:
  Record sounds of specific frequencies for all possible directions
  Normalise by recording with highest magnitude
  Connect resulting points on the polar plot
Polar response for an Omnidirectional microphone

## Slide 67: First Order Directional Microphones
First order microphones:
  Any microphone that has a polar response equation that has a cosine term to the first power
  Has a response proportional to the pressure gradient
The root mean square of the output voltage is given as:
  where is a dimensional constant, is the omni-directional component and is the pressure gradient component and represents the direction of the sound wave
By varying the values of and , different polar patterns or directional characteristics can be achieved

## Slide 68: The Cardioid
The polar pattern is more forward focused and captures most of the sound from the forward direction while rejecting most sounds from the back
Most commonly used microphone to capture speech and in musical performance
Polar response for the cardioid microphone

## Slide 69: The Supercardioid
Captures sound from the front only and the front beam is narrower than that of a cardioid
  increases the strength of the on axis signal
Polar response for the supercardioid microphone

## Slide 70: The hyper cardioid
this microphone captures the maximum from the forward direction, and provides the greatest rejection of off-axis components
Polar response for the hyper-cardioid microphone

## Slide 71: Microphone array speech processing
A microphone array is an arrangement of two or more microphones in a line, circle, sphere or other geometry
By using more than one microphone, it is possible to get:
  Increased directional polar responses
  Derive information such as the direction of arrival (DOA) of one or more sound sources
  Utilise multichannel speech enhancement algorithms
Sound source DOA estimation
Enhancement in the presence of multiple interfering sources
Application example: spatial sound scene recording

## Slide 72: Spaced microphone arrays
Spatial separation between each microphone
E.g. Uniform Linear Arrays (ULAs), Circular arrays, spherical arrays
Sound direction estimated by time difference of arrival (TDOA) of sound at each channel
E.g. for the ULA, direction, 𝜃 is calculated from the time difference of arrival, 𝜏, sensor spacing, d, and speed of sound in air, 𝑐≈340 𝑚/𝑠:
Download for free at http://cnx.org/contents/231a9c20-2afa-4faf-bc71-91396e66a573@4.4

## Slide 73: Spaced microphone arrays: Limitations
Spacing must be small enough to avoid spatial aliasing (analogous to temporal aliasing)
  Related to minimum wavelength of sound, , or maximum frequency,
E.g.
  for =1.6 kHz
    = 10.6 cm
  For =4 kHz
    4.25 cm
Distance, , must be known for applications such as DOA estimation, beamforming, etc.
Download for free at http://cnx.org/contents/231a9c20-2afa-4faf-bc71-91396e66a573@4.4

## Slide 74: Microphone array Beamforming
One key application of microphone arrays
Simplest type is delay-and-sum beamforming, which for a ULA with N microphones, the output is:
Where is the signal recorded by microphone and is time delay between the reference microphone (usually the first microphone) and the current microphone
Download for free at http://cnx.org/contents/231a9c20-2afa-4faf-bc71-91396e66a573@4.4

## Slide 75: Beamformers: Limitations
Beamformers are designed to maximise the quality of the recorded target sound, minimise influence of non-target sounds (noise, other sources, etc.)
Assuming minimum spatial sampling requirement is met, more microphones mean narrower main beams
  This is also frequency dependent
Can lead to arrays with lots of microphones and/or long physical lengths
  Undesirable for some applications
ULA beampattern, with 16 microphones, 2 kHz source
Single microphone breampattern

## Slide 76: Speech source Direction of Arrival (DOA) estimation: Applications
Source counting: How many people are speaking?
  Distinct DOAs can be used to count sources
Speaker diarization: who spoke when:
  DOAs can be used to label sections of speech corresponding to unique speakers
Speech source separation/speech enhancement
  Using DOAs to guide the separation of multichannel recordings into unique speech signal
  Can also be used for enhancing target speech in noisy and reverberant environments prior to other processes e.g. speech or speaker recognition
DOA estimation may not need to be too often (e.g. every 5 or 10 s)
DOA estimation may need to be more often (e.g. 25 ms for “real-time” speech communication applications
Easier!
Harder!

## Slide 77: Other types of microphone arrays
Co-incident microphone arrays: Microphones are co-located (or as close to each other as physically possible)
Ad-hoc microphone arrays: formed from randomly placed microphones in a room (e.g. the microphones attached to different people’s mobile phones)
Very large arrays e.g. spherical arrays with 32 or more microphones
Different arrays have different advantages, depending on the target application
UOW B-Format Array
Coresound Tetramic (http://www.core-sound.com/TetraMic/1.php)
Eigenmike:
https://mhacoustics.com/products

## Slide 78: DOA estimation using SRP-PHAT
Generalised cross-correlation (GCC) using PHAT weighting, where are the recorded signals for microphone and :
where
Sound source DOA estimation – based on finding the Time Difference of Arrival (TDOA) between pairs of microphones
In the figure, - for a source DOA arriving from an angle
TDOA corresponding to the largest steered response power (SRP):
DOA estimation using SRP-PHAT: NOTE: takes into account the discrete sampling, where the integral

## Slide 79: Want to no more – here is some suggested reading
Philipos C. Loizou, Speech Enhancement: Theory and Practice, Second Edition, CRC Press, 2013.
L.B. Rabiner and R.W. Schafer, Digital Processing of speech Signals, Prentice Hall, New Jersey, 1978.
Gibson, J., “Speech Coding Methods, Standards, and Applications”, IEEE Circuits and Systems Magazine, pp. 30-49, Fourth Quarter, 2005.
J. Benesty, M. M. Sondhi, and Y Huang (Eds.) Springer Handbook of Speech Processing, Springer Berlin Heidelberg, 2008.